## Slide 1: Networking, SDN, and OpenFlow: An Architectural Perspective
David Meyer
CTO and Chief Scientist, Brocade
Director, Advanced Technology Center, University of Oregon
March 2013
dmm@{brocade.com,uoregon.edu,1-4-5.net,…}

## Slide 2: Agenda
A Brief History of the (OF/SDN) Universe
What is Today’s OpenFlow?
What is the OpenFlow/SDN Architecture?
Thinking Architecture: Thin waists and hourglasses
Tomorrow’s OpenFlow/SDN Architecture?
Summary

## Slide 3: Danger Will Robinson!!!
This talk is intended to be controversial/provocative
(and maybe a bit “sciencey”)

## Slide 4: A Brief History of the OF/SDN Universe
Problem statement: Network architects, engineers and operators are being presented with the following challenge:
  Provide state of the art network infrastructure and services while minimizing TCO
SDN Hypothesis: It is the lack of ability to innovate in the underlying network coupled with the lack of proper network abstractions results in the inability to keep pace with user requirements and to keep TCO under control.
  Requirements stated informally, out of band, statically, …
  Better done by machine
    Obviously we need programmatic automation of config, monitoring, management, …
  For the most part true, but do we need to change the architecture to solve this?
  Hold that question…
So given this hypothesis, what was the problem?

## Slide 5: Maybe this is the problem?
Notes: (i). Every device is different; no common way of thinking about the data plane
(ii). Myopic view (box view vs network view)
(iii). Configuration and policy deeply intertwined  network is database of record and the like

## Slide 6: Or This?
Many protocols, many touch points, few open interfaces or abstractions,..
Network is Fragile, but is that the problem? BTW, what is fragility/robustness?

## Slide 7: History: How Did We Get Here?
Basically, everything networking was too vertically integrated, tightly coupled, non-standard.
Goes without saying that this made the job of the network researcher almost impossible
(before the era of overlays).
Question: Does the OF/SDN architecture map to the break down of vertical integration in
the compute world?

## Slide 8: (in)SANE
Slide courtesy Martin Cassado

## Slide 9: OpenFlow Switch, v 1.0 (Gates 104 Crew)
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
+ mask
Packet + byte counters
Flow Table
So question: Is this (architecturally) the same thing as the break-down of vertical
integration in the compute world?
“Flowmods at run-time”

## Slide 10: Trend (?)
Windows
(OS)
Windows
(OS)
Linux
Mac
OS
x86
(Computer)
Windows
(OS)
App
App
Linux
Linux
Mac
OS
Mac
OS
Virtualization layer
App
Controller 1
App
App
Controller
2
Virtualization or “Slicing”
App
OpenFlow
Controller 1
NOX
(Network OS)
Controller
2
Network OS
Computer Industry
Network Industry
Simple common stable hardware substrate below+ programmability + strong isolation model + competition above = Result : faster innovation
Slide Courtesy Rob Sherwood
Notes: 10

## Slide 11: Well…OF/SDN Architecture
App
Simple Packet Forwarding Hardware
Simple Packet Forwarding Hardware
Simple Packet Forwarding Hardware
App
App
Simple Packet Forwarding Hardware
Simple Packet Forwarding Hardware
OpenFlow Controller
11
Control plane
Data plane
OpenFlow Protocol
App
App
Graphic courtesy Nick Mckeown
Separation of Control and Data Planes
Open Interface to Data Plane
(logically) Centralized Control (?)
“NB API”
Notes: Switches, routers and other middleboxes are dumbed down
The key is to have a standardized control interface that speaks directly to hardware

## Slide 12
Graphic courtesy James Hamilton,
http://mvdirona.com/jrh/TalksAndPapers/JamesHamilton_POA20101026_External.pdf
So Same as What Happened in Compute?
Doesn’t Look Like It

## Slide 13: BTW, Logically Centralized? (hint: logically centralized means distributed)
Graphic courtesy Levin, D., et. al., “Logically Centralized? State Distribution Trade-offs in Software Deﬁned Networks?”,
HotSDN 2012, http://conferences.sigcomm.org/sigcomm/2012/paper/hotsdn/p1.pdf
Key Observation: Logically centralized  distributed system  tradeoffs between
control plane convergence and state consistency model. Note that this is beyond
the responsiveness lower bound: Ω(RTT(switch, controller)+ppt(switch)+ppt(controller))

## Slide 14: BTW, Nothing New Under The Sun…
Separation of control and data planes is not a new idea. Examples include:
  SS7
  Ipsilon Flow Switching
    Centralized flow based control, ATM link layer
    GSMP (RFC 3292)
  AT&T SDN
    Centralized control and provisioning of SDH/TDM networks
  A similar thing happened in TDM voice to VOIP transition
    Softswitch  Controller
    Media gateway  Switch
    H.248  Device interface
    Note 2nd order effect: This was really about circuit2packet
  ForCES
    Separation of control and data planes
    RFC 3746 (and many others)
  …

## Slide 15: So Reality: What Is OpenFlow?
A Switch Model
  Match-Action Tables (MAT)
    How many, How they are connected, table attributes, etc
  Per-flow counters
An Application Layer Protocol
  Binary wire protocol, messages and state machine that allow programming of the MAT
A Transport Protocol
  TLS, TCP, ..
OF says nothing about how a given forwarding target implements the switch model
   OF is an Abstract Switch Model
  As we’ll see later, I argue that OF is built on the wrong set of abstractions

## Slide 16: Thinking Architecture/Complexity (Bowties and RYF-Complexity)
Notes: (i). Every device is different; no common way of thinking about the data plane
(ii). Myopic view (box view vs network view)
(iii). Configuration and policy deeply intertwined  network is database of record and the like

## Slide 17: Robustness vs. Complexity Systems View
Increasing number of policies, protocols, configurations and interactions
Domain of the fragile
Domain of the Robust
Can we characterize the Robust and the Fragile?

## Slide 18: Thin Waists 101: The Bowtie Architecture Ideas from Systems Biology Constraints that Deconstrain
For example, the reactions and metabolites of core
metabolism, e.g., ATP metabolism, Krebs/Citric Acid
cycle signaling networks, …
See, e.g., Doyle, et. al., “Architecture, Constraints, and Behavior”, http://www.pnas.org/content/108/suppl.3/15624.full

## Slide 19: But Wait a Second Anything Look Familiar?
Hourglass Architecture
Bowtie Architecture

## Slide 20: So Where Does OF/SDN Fit?
Maybe here?

## Slide 21: Robustness and Fragility
Definition: A [property] of a [system] is robust if it is [invariant] with respect to a [set of perturbations], up to some limit
Fragility is the opposite of robustness
  If you're fragile you depend on 2nd order effects (acceleration)
  A bit more on this in a sec…
A system can have a property that is robust to one set of perturbations and yet fragile for a different property and/or perturbation  the system is Robust Yet Fragile (RYF-complex) [0]
  Or the system may collapse if it experiences perturbations above a certain threshold (K-fragile)
Example: A possible RYF tradeoff is that a system with high efficiency (i.e., using minimal system resources) might be unreliable (i.e., fragile to component failure) or hard to evolve
[0] http://www.istar.upenn.edu/osw/white paper/John Doyle White Paper.pdf

## Slide 22: RYF?

## Slide 23: RYF Tradeoffs

## Slide 24: Key Architectural Takeaways
The fundamental architectural building blocks of systems that scale and are evolvable include
  Bowties/hourglasses architectures with RYF complexity
  Massively distributed with robust control loops
  Highly layered
  Protocol Based Architecture (PBA)
  Degeneracy
OF/SDN?
  Centralized (at least “logically”)
  Delayered
  “Protocol Agnostic”
  Non-degenerate
    In fact, consider NfV in this context…

## Slide 25
Review: OF Version 1.0
Drop
Flow Table
(TCAM)
Redirect to Controller
Forward with
edits
Packet
Apply actions
Encapsulate packet to controller
Too simple:
Feature/functionality
Expressiveness/Lossy Abstractions

## Slide 26: OK, Fast Forward to Today: OF 1.1+
Why this design?
  Combinatoric explosion(s) s/a routes*policies in single table
However, intractable complexity: O(n!) paths
  c ≈ a(2^l) + α
  where a = number of actions in a given table, l = width of match field, and
  α all the factors I didn’t consider (e.g., table size, meta-data, group tables)
Too complex/brittle
  Algorithmic complexity
  What is a flow?
  Not naturally implementable on ASIC h/w
  Breaks new reasoning systems
  No fixes for lossy abstractions (next slide)
  Architectural questions
So question: Is the flow-based
abstraction “right” for general
network programmability?

## Slide 27: Lossy OF Abstractions
Problem: Current versions of OF do not work well on ASIC forwarding targets
Why? Basically, the simple abstraction of setting forwarding table entries looses too much information about the application developer's intent, making it difficult (or impossible) to leverage switch features to deliver scalable and efficient end-to-end implementations
Issues with the 1.X Abstractions
  Information Loss
    Controller to switch
  Information Leakage
    Switch to controller
  Weak Control Plane to Data Plane Abstraction
  Combinatorial State Explosion
  Data Plane Driven Control Events
  Weak Indirection Infrastructure
  Time Sensitive Periodic Messaging
  Multiple Control Engines
  Weak Extensibility
  Missing Primitives
OF 1.X abstractions are “lossy” and as such can’t take advantage of ASIC features
  As a result a controller must include platform specific code  brittle implementations
  Specifies too much of “how” the switch should operate (as opposed to “what” it should be doing)

## Slide 28
Lossy OF Abstractions
Graphic courtesy Dan Cohn

## Slide 29: History of a Solution Google OF 2.0 Proposal
Google proposal was a producer/consumer DAG model
  Just like today’s OF 1.1+ only richer
    OF 1.1+ can only express an implicit linear “DAG” table organization (with conditionals)
    Google model can express Conditional, Serial, Parallel and Speculative pipelines
    OF 1.1+ has a restricted set of primitives (basically flow_mods)
  Producer/Consumer relationship between primitive “blocks”
    “blocks” built up from rich set of primitives (example on next slide)
  Expresses the ordering constrains (if any) to the target
  Conveys the minimum set of constrains

## Slide 30: Example: Shared Table Primitives (pseudo-code)
primitive TABLEDEF (Name = "MACTable",
TableShared = TRUE,
TableType = ExactMatch,
SearchKey = {{(VlanID, 12), (MACAddress, 48)}, /* bridging */
{(PortID, 8), (VlanID, 12), (MACAddress, 48)}}, /* learning */
TableRsult = {BridgingResult,LearningResult},
TableSize = MacTableSize);
Then to match against such a table for a learning bridge you'd have a primitive operation like:
primitive TABLEOPS_MATCH(MatchName = LearningBridgeMatch,
TABLE = "MACTable",
consumes(PortID, VLANID, MACSrcAddress),
SearchKeyMap = {((PortID:PortID),
(Vlan:VlanID),
(MACAddress:MACSrcAddress))},
produces(LearningHit),
ResultMap = {(LearningResult:LearningHit)});

## Slide 31
Putting it All Together
Google OF 2.0 Model
Graphic courtesy Dan Cohn

## Slide 32: Beautiful idea, but….
Was seen as too dynamic/futuristic by the ONF TAG
A “dumbed down” version was proposed
  Basically less dynamic
    No runtime composition of models
    No language to express primitives and their compositions
  Small set of pre-defined models
  Was still seen as too ambitious
Current ONF direction is to add “table typing” to OF 1.3+
  The capability to constrain a table to be one of exact match, wildcard, LPM, …
  Along with Table Type Patterns (TTPs)
    A graph plus properties/constraints representing how tables are connected, …
  This is the work of the Forwarding Abstractions Working Group
BTW, isn’t this converging on ForCES?
  And why hasn’t ForCES succeeded?

## Slide 33: Summary
Only OF 1.0 “widely” implemented
  Widely a relative term
  A few new software implementations of 1.3
    e.g., LINC, others
    See http://www.flowfowarding.org
OF 1.1+ not widely implemented in h/w
  Only know of a few implementations
    Most h/w implementations on NPU-like h/w, so really s/w
ONF direction “could” yield something
  “table typing” could be a part of a solution
  Getting the abstractions right is the key
    And of course, getting the abstractions right is one of the hardest parts of all of this
Many open questions remain regarding architecture/scalability
  Both of OF itself and of the OF/SDN architecture
  Bowties, RYF systems
What about other network programmability architectures?
   Emerging SDN Continuum

## Slide 34: Future (now): The SDN Continuum
DP/SDN
Properties:
-- Complete Separation of CP and DP
-- Open Interface/programmable Data Plane
-- Examples: OF, ForCES, various control platforms
-- Initially: Applications program the network
OL/SDN
Properties:
-- Retains existing (simplified) Control Planes
-- Programmable overlay control plane
-- Examples: Various Overlay technologies
-- May use OF to program flows in vSwitch
CP/SDN
Properties:
-- Retains existing (distributed) Control Planes
-- Programmable control plane
-- Network aware applications
Explicitly *not* e.g., learning switch
-- Examples: PCE, I2RS, vendor SDKs
Physical and Virtual Resources
(CSN)
Control and Orchestration
(overly simplified view)
Apps
Apps
…
Service Layers
May be repeated
(stacked or recursive)
Notes: OF/SDN is a polar architectural design point; complete separation of control and data planes
CP/SDN is adds programmability in an incremental way to conventional control planes; some targeted separation (e.g., PCE)/centralization
OL/SDN (Overlay/SDN) retains the control plane architecture of CP/SDN but adds a new, logically centralized control plane (“over” CP/SDN)

## Slide 35: Q&A
Thanks!